## Slide 1
Comparison and Implementation of Data Compression Methods for SoC-based Radar Systems
Author: Jordan Mohindra
Supervisor: A/Prof Beena Ahmed
2026 Thesis Project
Why compress radar data?
Cascaded MIMO radars (here 12 transmitters × 16 receivers) produce very high data rates: 3.2 Gbit/s in Kiem's system [1].
The link to the car's central computer (SoC) becomes the bottleneck: bandwidth, power and delay.
So: compress at the sensor, losslessly. Less data on the link, identical data after decoding, so target detection is unchanged.
Radar
393 KB / frame
FPGA
compress
SoC
decompress
93 KB
same data, bit for bit
What are DRHE and LPC?
Both predict each sample from earlier chirps of the same transmitter, then Huffman-code the small prediction error. The decoder makes the same prediction and adds the error back, so nothing is lost.
DRHE (Kiem [1]): fixed filters predict the magnitude and phase from the previous ramps. Works as the data streams in.
LPC: fits 2 coefficients per range bin to the whole frame: x[m] ≈ a₁·x[m−12] + a₂·x[m−24].
Why these two? In the MATLAB screen (step 2) they were the only lossless methods with a compression ratio above 3.
[Photo: KCU116 FPGA board and laptop running the test]
Method → Results
1
Real radar data
ColoRadar recordings [2] from a TI AWR2243 cascade (12 TX). Range FFT in MATLAB, then 16-bit frames.
2
Screen 8 algorithms
MATLAB: compression ratio and target detection for every method on 50 frames.
3
DRHE vs LPC
Where does the compression come from? Huffman coding, prediction, and a dictionary re-derived for this data. The dictionary helps more than the predictor.
4
Build it in hardware
C++ in Vitis HLS → Vivado → AMD KCU116 FPGA. Encoder and decoder on the chip.
5
Measure on the board
Stream 50 frames through the FPGA, check every frame is bit-exact, and time it.
Input: one frame = 128 range bins × 192 ramps × 4 RX, 16-bit I/Q = 393 KB
Output: a compressed bitstream of about 93 KB (DRHE). Decompressing it gives back exactly the same frame.
The green area is the goal: high compression (right) and no extra missed targets (bottom).
Lossy methods (BAQ, RDVLE) shrink the data but lose targets. Only DRHE and LPC land in the green.
The 3.77 % baseline comes from 16-bit rounding, not compression.
Encoder + decoder use under a quarter of the chip: DRHE 23 %, LPC 25 % of the logic (LUTs).
The same C++ that was simulated runs on the FPGA, so the hardware can be checked bit for bit against the simulation.
50 / 50 frames bit-exact on the FPGA
DRHE: 0.61 ms per frame. Output streams out as the data comes in.
LPC: 3.25 ms per frame. It must store the whole frame before it can output anything.
Decode timing: board run pending.
Why an FPGA, not just simulation?
Compression has to run at the sensor, in real time, on small low-power hardware.
Simulation cannot show speed, latency or chip size.
Hardware proves the design reproduces the simulation bit for bit. Kiem's did not (3.25 in simulation, 3.17 on hardware [1]).
Conclusion
Both DRHE and LPC are lossless on real radar data, on real hardware.
LPC compresses most: 4.40× (DRHE 4.22×). Re-deriving the Huffman dictionary for this data helped more than the predictor did.
DRHE streams with no frame buffer; LPC must buffer a whole frame (3.25 ms). Both meet the 15 ms limit here, but DRHE scales better to bigger frames.
Next: a streaming LPC, all 16 receivers, fixed-point DRHE.
[1] L. Kiem, Design and Implementation of Data Compression Methods for SoC-based Radar Systems. [2] A. Kramer et al., ColoRadar: the direct 3D millimeter wave radar dataset, IJRR, 2022.